## Slide 1
Everything Is Possible Here For Customized S7000

## Slide 2
S-7000P Pin Insertion Machine
Automatic
Stable Quality
High Output
PCB Auto loader/unloader
PC Controller with Windows System
Servo Motor Drive
Visual on-line Programming
Visual Component Inspection
Auto Visual Correction
Missing Part detection
High ROI
Help To Build A Smart Factory

## Slide 3
Equipment size | 1660mm*1600mm*1530mm
Packaging | Reel tape terminal
Equipment weight | 1500KG
PCB size | 380mm*280mmm (enlarged size can be customized)
Number of insertion heads | 1-4 Optional
terminal thickness | ≥0.5mm ≤1.2mm
Vertical error | ≤0.8°
Insertion angle | 360°( increment 1°)
Body distance | The distance between the components ≥ 2mm
Humidity | 30%-70%
Display system | 17-inch color LCD monitor
Feeding system | Tape feeder + feeding guide
Motion accuracy | 0.001mm/pulse
Motion system | Panasonic controller, motor
Programming function | Online visual programming, visual correction, EXCEL
Data import | USB interface import, manual entry
Communication interface | RS-232C (can be connected to MES system)
Power | Single 220V/AC, 50/60HZ, 2KVA
Machine specifications

## Slide 4
TE Action Pin & Bear Board
Bear Board Size: 244mm*230mm
Total Pins on 1 Board: 32*3=96 pcs
PN: 1-928776-5

## Slide 5
Reel Tape Feeder
Insertion Head
Machine details

## Slide 6
Tape feeder
Tterminal insertion head
Similar Machine Configuration

## Slide 7
Capacity calculation
PCB | Number of devices | Number of components (Faston/single panel) | CPH | component/s | Single PCB panel Insertion time(s) | UPH (PCB) | Remarks
 | 1 set S-7000P | 96 | ~8000 | ~0.45 | ~43.2 | ~67 | Cycle time includes: PCB entry and exit(4s) and MARK recognition(1s) .UPH of PCB is about 67 pcs （3600s÷(43.2s+4s+1s）*90%）
PCB production ( per day 20 hours): 1340 pcs |  |  |  |  |  |  | 
Estimated Capacity
* 90% means that the machine production speed is not the fastest, Only 90% efficiency.

## Slide 8
PIN Insertion Video

## Slide 9
PIN Insertion Line
S-7000P Pin Component Inserter Machine
SLD250
SULD250

## Slide 10
Standard magazine loader
Board handing system loader serial
Model | Dimension (L*W*H.MM) | PCB size(MM) | Weight(KG) | Rack size(L*W*H.MM)
SLD250 | 1800*970*1250 | 50x50-530x460 | 300KG | 535*530*563
Features
This unit is used for loading of PCBs from the production line.
Description
Specifications
Schematic
Sturdy and stable design
User friendly ‘soft touch’ LED membrane control panel
Pneumatic clamps provided for magazine alignment
Pneumatic pusher’s pressure regulated
High throughput with short magazine change-over time
SMEMA compatible

## Slide 11
Sturdy and stable design
Magazine quantity: upper 1pc, bottom 1pc.
Tank Replacement time: about 30 seconds or specify
Step select: 10,20,30,40 mm or specify
Spec. 110V or 220V, single phase max 250VA.
Barometic pressure from 4-6 bar, up to 10/min
Flexible platform to suit standard magazines.
Regulated pressure on attached pneumatic pusher.
Pusher position adjustable to centre of the magazine.
User friendly “soft touch” LED membrane controlpanel.
SMEMA compatible
Standard magazine unloader
Board handing system unloader serial
Model | Dimension (L*W*H.MM) | PCB size(MM) | Weight(KG) | Rack size(L*W*H.MM)
SULD250 | 2660*970*1250 | 50x50-530x460 | 320KG | 535*530*563
Features
This unit is used for unloading of PCBs from the production line.
Description
Specifications
Schematic

## Slide 12
Best After-sales service
— 7x24 Worldwide Support
— Free Installation/ Training
— 1 day lead-time (spare parts)
— 1 Month customize solution

## Slide 13
Please visit
WELCOME INQUIRY
www.smthelp.com
Find us more
https://www.facebook.com/autoinsertion
Know more our team
https://cn.linkedin.com/in/smtsupplier
Welcome to our factory in Shenzhen China
See more machine working video, please Youtube
Google
Looking forward to your email
Auto+insertion, to get more information
info@smthelp.com
Auto Insertion