## Slide 1
S-7000T Terminal Insertion Machine

## Slide 2
S-7000T Terminal Insertion Machine
Fast Facts
Insertion rates up to 2 per second at 0.2 in (5.08 mm) pitch.
Up to 4 different compo­nents can be applied in one machine
Apply products at up to 4 different angles
insertion verifi­cation, and Inward clinching/Outward clinching/”N”. (Optional)
Windows-based 17-inch color LCD monitor
Quick change head system, allow production flexibility. (Optional)
Able to process any manufacturer's reeled through-hole
High-speed servo drives for insertion rates up to 5 cycles per second at 0.2 in (5.08 mm) pitch.
Take two insertion heads as an example, a total of 7 Panasonic servos.
FA/FB: Control the two insertion heads.
X0, Y1: Control the worktable.
RA2, RB4: Control the rotation angle(1-360°) of the insertion head.
Q3: Control the rotation angle(1-360°) of the clinching model.
Three motors control the PCB input, PCB output, and worktable.
Visual system: Industrial specialized high definition camera and the development of automatic visual correction software of vision system, automatic correction, insertion accurately.
Operating system: Industrial computer + motion control card.
Windows environment to run the operation of the software, the production data, management data, equipment parameters, all I/O signal diagnosis, etc. can be finished on the host.
PCB board handling equipment(loader+unloader machine) ready for Industrial 4.0.
Pass the IPC-9704 stress test standard to ensure that the stress value of each insertion is within ±400.

## Slide 3
S-7000T Terminal Insertion Machine(two insertion heads)

## Slide 4
S-7000T Terminal Insertion Machine(two insertion heads)
Physical dimensions.
Width: 1300 mm
Heigth: 1600mm (door close)
Depth: with out reel feeder 1700mm
with reel feder 2560 mm. Weight: 1200 kg. (with out reel feeder) Reel feeder weight: 60 kg

## Slide 5
Equipment size | 1700mm*1300mm*1600mm (2 heads)
Packaging | Tape terminal, bulk terminal
Equipment weight | 1200KG
PCB size | 380mm*280mmm (enlarged size can be customized)
Number of insertion heads | 1-4 Optional
terminal thickness | ≥0.5mm ≤1.2mm
Vertical error | ≤0.8°
PCB requirements | The insertion hole is 0.5±0.1mm larger than the component foot
Insertion angle | 360°( increment 1°)
Body distance | The distance between the components ≥ 2mm
Clinch | Inward clinching/Outward clinching/”N”
Humidity | 30%-70%
Display system | 17-inch color LCD monitor
Feeding system | Tape feeder or Bowl feeder + feeding guide
Motion accuracy | 0.001mm/pulse
Motion system | Panasonic controller, motor
Programming function | Online visual programming, visual correction, EXCEL
Data import | USB interface import, manual entry
Communication interface | RS-232C (can be connected to MES system)
Power | Single 220V/AC, 50/60HZ, 2KVA
Machine specifications

## Slide 6
Feeding and Cutting system
Design tape feeder according to the terminal width
Material tray
Feeding track(L)
Feeding track(R)

## Slide 7
Feeding and Cutting system

## Slide 8
Feeding and Cutting system

## Slide 9
Feeding and Cutting system

## Slide 10
Design insertion head according to the terminal thickness
Different terminal thickness(0.80mm
/0.50mm) designs different grippers
Insertion system

## Slide 11
Insertion system

## Slide 12
Clinching system
(if the detection system detects that the insertion has completed successfully Go to the next step, if it is not completed, the machine will stop and report an error.) After that, the X-Y workbench will send the PCB completed by the insertion to the right track

## Slide 13
Software programming system
The main operation interface is divided into the following six areas from top to bottom, left and right.
Operation panel area
Image and video area
Production data area
Program display area
Status prompt area
Set up ribbon

## Slide 14
Application industry
Home appliance industry
The car industry
The power industry
Other electronics industry: digital watches,electronic components, etc

## Slide 15
Best After-sales service
— 7x24 Worldwide Support
— Free Installation/ Training
— 1 day lead-time (spare parts)
— 1 Month customize solution

## Slide 16
Please visit
WELCOME INQUIRY
www.smthelp.com
Find us more
https://www.facebook.com/autoinsertion
Know more our team
https://cn.linkedin.com/in/smtsupplier
Welcome to our factory in Shenzhen China
See more machine working video, please Youtube
Google
Looking forward to your email
Auto+insertion, to get more information
Ronin@smthelp.com
Auto Insertion