## Slide 1
Shenzhen Southern Machinery Solder Paste test report

## Slide 2
Table of contents
Equipment introduction
Introduction of the valve body
Application scenarios
Comparison of valve types
Test data
Video and tin spot effect

## Slide 3
1、Equipment introduction
Technical Features:
● Positioning accuracy: ±30µm@4σ;
● Repeatability: ±15µm@4σ;
● Support range: 350*550*40mm
● Piezo valve non-contact jet dispensing/screw valve
● High speed, jetting speed up to 1000 dots/second, minimum dispensing volume 2nL
● Small size, occupying an area of only 1㎡
● 3C industry applications such as mobile phones, smart wearables, and PCB boards
S-D5

## Slide 4
2、Introduction of the valve body-- needle valve
GZ50
Technical characteristics of high-precision dispensing machine to deal with viscosity changes
● Control mode: timing mode/manual control mode
● Discharge pressure setting range: 0.030～0.500MPa
● Dispensing time setting range: 0.001～9999.999s
● Vacuum pressure setting range: 0～-0.020MPa
● The smallest point diameter of spot tin is 0.15mm
● Main functions: automatic compensation of liquid level difference, automatic prevention of liquid leakage, automatic remaining volume warning, vacuum pressure correction

## Slide 5
2、 Valve Body Introduction--Helding Tin Piezoelectric Valve
● Technical Features:
● Injection frequency: max 500Hz (can be set)
● Minimum spot diameter: 0.22 mm (6#)
● Dispensing accuracy: ±5%
● Applicable solder paste range: 5#/6#/7#/8#---solder paste powder
● Parts can be replaced online
● Seal maintenance cycle: 7-15 days
In response to the dispensing application of solder paste in SMT placement technology, Nanfang Machinery has developed a high-precision, cost-effective, and stable performance piezoelectric valve for solder paste.

## Slide 6
2、Valve Body Introduction--Screw Valve
Southern Machinery Screw Valve:
SAC-100Features: high control precision, fast response to glue output, suitable for contact dispensing process with tight glue output·
●Maximum speed: 800r/min
● Minimum glue output: 0.2ml
● Minimum point diameter: 0.15mm
● Glue volume accuracy: M±5%
● Runner quick release structure
Seal maintenance cycle: about 30 days
It has the function of reverse rotation and suction, and is widely used in solder paste,Medium and high viscosity fluids such as red glue, silver paste, thermal conductive silicone grease, etc.

## Slide 7
3、Application Scenario
Application Scenario | application glue type | 
Precision instruments, electronic equipment precision glue control | Conductive silver paste | √
Can be used for surface mount of PCB/FPC in SMT industry | Washable Flux Paste | √
Tin filling of solder joints of electronic components such as IC modules | Die Bonding Solder Paste | √
Lens bonding in the LED industry | Laser Solder Paste | √
Component Repair | Stainless steel solder paste | √
Spray glue in the gap of special-shaped products | Other special solder paste/silver paste for dispensing | √

## Slide 8
4、 Comparison of Valve Types
Point diameter requirements | Solder Paste Type | valve type | applicability | Advantages and Disadvantages
0.15-0.3mm | 5#、6#、7#Power | GZ50 needle valve | High-value products with high tinning requirements | Moderate speed, good solder paste forming, small dot diameter, medium cost
0.2-0.5mm | 6#、7#、8# Power | Piezoelectric tin spray valve | High requirements on point diameter and wire diameter, and fast speed | Fast speed, small spot diameter, high cost of use
>0.5mm | 4#、5# Power | screw valve | Common applications that do not require high tin points | Slow speed, poor molding, low cost of use, and simple maintenance

## Slide 9
5、 Test data
 | Test Methods | Needle needle 0.15mn | Piezo valve nozzle 0.1mm striker 1.0mm | Screw valve needle TE20G
5# powder | Point：The minimum dot diameter is 10*10 dot matrix, stable tin production | N/A | N/A | 0.50mm-0.55mm
 | Square wave: minimum diameter, height 6mm, width 3mm square wave | N/A | N/A | 0.51mm-0.55mm
 | Keel type: minimum wire diameter, segment length 15mm, interval 2mn*10 | N/A | N/A | 0.53mm-0.55mm
6# powder | Dot: minimum dot diameter 10*10 dot matrix, stable tin | 0.24mm | 0.22mm-0.25mm | N/A
 | Square wave: Minimum wire diameter, 6mm high, 3mm wide square wave | N/A | 0.45mm-0.52mm | N/A
 | Keel type: minimum wire diameter, segment length 15mm, interval 2mm*10 | N/A | 0.37mm-0.39mm | N/A
7# powder | Dot: minimum dot diameter 10*10 dot matrix, stable tin | 0.2mm | 0.20mm-0.23mm | N/A
 | Square wave: Minimum wire diameter, 6mm high, 3mm wide square wave | N/A | 0.41mm-0.50mm | N/A
 | Keel type: minimum wire diameter, segment length 15mm, interval 2mm*10 | N/A | 0.35mm-0.38mm | N/A

## Slide 10
6. 0.2mm point diameter test video of 7# powder 6.1

## Slide 11
6、Effect picture 6.2
0.15mm Wire diameter

## Slide 12
6. 6# powder 0.2mm wire diameter test video 6.3

## Slide 13
6、Effect picture 6.4
0.2mm Wire diameter

## Slide 14
6. 5# powder 0.3mm wire diameter test video 6.5

## Slide 15
6、Effect picture 6.6
0.3mmWire diameter

## Slide 16
Best After-sales service
— Free Installation/ Training
— 1 day lead-time (spare parts)
— 5 days customized design
— 7x24 Worldwide Support

## Slide 17
Please visit
WELCOME INQUIRY
www.smthelp.com
Find us more
https://www.facebook.com/autoinsertion
Know more our team
https://cn.linkedin.com/in/smtsupplier
Welcome to our factory in Shenzhen China
See more machine working video, please Youtube
Google
Looking forward to your email
Auto+insertion, to get more informations
info@smthelp.com
Auto Insertion