## Slide 1
Low cost Auto Insertion Solutions
Professional THT
Worldwide support
Free Installation and Training
Free THT design guidance

## Slide 2
Up to 22,000 cph
Off-line/In-line operation availability
Using imported precision ball-screw & AC Servo
system, positioning accuracy <0.001mm
Vision system for positioning and insertion alignment
Accurate insertion angle in 0-360º,with 1ºincrement
Integral forming cast iron machine frame
Multiple lead span combination available：2.5/5.0mm; 2.5/5.0/7.5mm; 5.0/7.5/10.0mm; 2.5/3.5/5.0mm; 2.5/5.0/7.5/10.0mm
Option of automatic error recovery
Long lifetime insertion driving axis structure
Compatible with Universal insertion m/c feeder
USB port for data transfer & Excel format compatible
S-3000 Radial Insertion Machine

## Slide 3
S-3010
Off Line/in line
High speed
Radial insertion m/c
10 feeders only

## Slide 4
Dimension L1750 x W1450 x H1700mm(Off-Line)
Dimension L1920 x W1450 x H1700(In-Line)
Weight: 1150kg
Feeder Module L1800 x W1450 x H1100mm
Machine Outline & Size

## Slide 5
Toothed bar driving axis，reduce cost and easy alignment
2000W motor driving,higher insertion speed
Accurate insertion angle in 0-360º,with 1ºincrement
Cover 4 different lead span 2.5/5.0/7.5/10.0mm
Insertion depth programmable
Servo driven component transfer to main claw structure(CTA)
Insertion HEAD

## Slide 6
1.2/1.5/1.8mm lead length selectable, 10-35ºclinch
3.5mm lead span components
Inward/outward clinch
Servo driven cut & clinch module up/down
Lead scrap collection mechanism
Cut & clinch HEAD

## Slide 7
360º clockwise/counter clockwise rotation table (Off-line m/c)
PCB size Min: 50x50mm ; Max: 450x450mm
Non-stop PCB loading
Work board holder or
Board handling System
BHS
WBH
Auto PCB load/unload, width adjustable conveyor(On-line m/c)
PCB size Min: 50x50mm ; Max: 400x285mm
SMEMA interface

## Slide 8
0.3 mega pixel, 256 grey scale industrial camera for vision system
Fiducial mark recognition for positioning and alignment
Vision automatic align insertion position
Position deviation less than 0.001mm
vision Position correction

## Slide 9
750W Panasonic servo motor, high speed & stable
Strengthened chain tension adjustment, convenient for adjustment
107 pcs longer lifetime component carrier clips(Consumable parts)
SEQUENCER chain

## Slide 10
Servo motor, high speed & stable
Strengthened chain tension adjustment, convenient for adjustment
longer lifetime component carrier clips(Consumable parts)
SEQUENCER chain

## Slide 11
Radial Lead Component Feeder
10/20/30/40/60/80 Component stations
Compatible with Universal insertion m/c feeder
New designed,reduce component jam possibility
Fast changeover ， convenient for maintenance
Feeder add-on retrofit availability after ex-factory

## Slide 12
New designed to guaranteed lead cutting verticality & long lifetime
Improving tape clamp & remove structure
Convenient for alignment & maintenance
Tape cutter station

## Slide 13
Electronic controller
Japan servo driving system
Windows 7 system
Industrial computer control with Chinese/English
interface
Option of remote control availability

## Slide 14
programming
USB port for data transfer, Gerber format (Excel)file input, program automatically created
Vision on line teaching position, automatically align position

## Slide 15
Service Requirements
Power requirement:AC220V, 50/60Hz, 1.5Kw
Maximum Neutral to Earth Ground voltage is limited to 5VAC.
Compressed air requirement 0.6 Mpa 0.3m3/min
Non-lubricated, dry air, dew point must be at 11°C (51°F) below ambient temperature

## Slide 16
Machine Working Video
More Radial machine video, Please Youtube: Auto Insertion
— List Price $70K
— Worldwide Support
— Free Installation/ Training
— Auto PCB loading
— 6 Months ROI

## Slide 17
Welcome inquiry
1,Please visit : www.smthelp.com
2, Find us more: https://www.facebook.com/autoinsertion
3, Know more our team: https://cn.linkedin.com/in/smtsupplier
4, Welcome to our factory in Shenzhen China
5, Look at more machine running video:https://www.youtube.com/jasonwuSMT
4, See more in Google: Auto+Insertion