## Slide 1
Are you still coping with the MANUAL insertion headaches:
*Low efficiency
*Poor quality
*Difficult processing
*High defective and scrap rate
*High manufacturing costs
S7020 Series Insertion Machine

## Slide 2
S7020 Series Insertion Machine
1.S7020T Terminal Insertion machine (2 insertion heads and 2 reel feeder / or 2 bowl feeder)
2.S7020E Eyelet Insertion machine (2 insertion heads and 2 Bowl feeder)
3.S7020P PIN Insertion machine (2 insertion heads and 2 reel feeder / or 2 Bowl feeder)
4.S7020S Tact Switch Insertion machine (2 insertion heads and 2 Bowl feeder)
5.S7020F Oddform Insertion machine (2 insertion heads and 2 Bowl feeder /or 2 tube feeder)
S7020 Series Insertion Machine-a Multifunctional Combination
I 'll never say tired,
just need regular
maintenance !

## Slide 3
Specifications
– Speed: 12,000 CPH
– PCB Size: Max. 400mm * 400mm
– PCB Thickness: 0.76-2.36mm
– Components available: Pin,Tact Switch,Terminal, Eyelet
– 2 Heads
– Machine dimension: 1220mm*1000mm*1600mm (L*W*H)
– Machine weight: 1500KG
– Power supply: Single Phase 220VAC, 50/60HZ, 1.0KVA
– System Protection: Built-in software protection
– Air pressure: 0.4-0.6Mpa/0.3M3/Min
– Data input: USB interface input (EXCEL format)
– Control System: English version interface (WINDOWS system control platform) LCD monitor
– PCB transfer mode: automatic (left to right or right to left)
*One machine can replace at
least 10 labors
*Price 30% lower than foreign brands
*Faster speed, lower maintenance cost
*Simple operation, grasp with1 day training
S7020 Series Insertion Machine

## Slide 4
Tape feeder
Terminal mold
Structure
S7020 Series Insertion Machine

## Slide 5
Vision programming
Clinching base(PCB support& miss check)
Inserion head
Feeder
S7020 Series Insertion Machine

## Slide 6
Machine Insertion Head ASSY
Connect to motor
Programming camera
Head driver
Nozzle
L cutter
R cutter
Pedestal
S7020 Series Insertion Machine

## Slide 7
Clinching system
If the detection system detects that the insertion has completed successfully Go to the next step, if it is not completed, the machine will stop and report an error.) After that, the X-Y workbench will send the PCB completed by the insertion to the right track
S7020 Series Insertion Machine

## Slide 8
Feeding and Cutting system
Change feeder/gripper according to the component
Material tray
Feeding track(L)
Feeding track(R)
S7020 Series Insertion Machine

## Slide 9
Application industry
Home appliance
Car
Power
Digital watches
Electronic components, etc
S7020 Series Insertion Machine

## Slide 10
Best After-sales service
— 7x24 Worldwide Support
— Free Installation/ Training
— 1 day lead-time (spare parts)
— 1 Month customize solution

## Slide 11
Please visit
Welcome Inquiry
www.smthelp.com
Find us more
https://www.facebook.com/autoinsertion
Know more our team
https://cn.linkedin.com/in/smtsupplier
Welcome to our factory in Shenzhen China
See more machine working video, please Youtube
Google
Looking forward to your email
Auto+insertion, to get more information
info@smthelp.com
Auto Insertion